## Slide 1: Chapter 5. Synchronous Sequential Logic Part A

## Slide 2: Combinational circuits
So far we’ve just worked with combinational circuits, where applying the same inputs always produces the same outputs.
This corresponds to a mathematical function, where every input has a single, unique output.
In programming terminology, combinational circuits are similar to “functional programs” that do not contain variables and assignments.
Combinational
circuit
Inputs
Outputs

## Slide 3: Sequential circuits
In contrast, the outputs of a sequential circuit depend on not only the inputs, but also the state, or the current contents of some memory.
This makes things more difficult to understand, since the same inputs can yield different outputs, depending on what’s stored in memory.
The memory contents can also change as the circuit runs.
We’ll some need new techniques for analyzing and designing sequential circuits.
Combinational
circuit
Inputs
Memory
Outputs

## Slide 4: Examples of sequential devices
Many real-life devices are sequential in nature:
  Combination locks open if you enter numbers in the right order.
  Elevators move up or down and open or close depending on the buttons that are pressed on different floors and in the elevator itself.
  Traffic lights may switch from red to green depending on whether or not a car is waiting at the intersection.
Most importantly for us, computers are sequential! For example, key presses and mouse clicks mean different things depending on which program is running and the state of that program.

## Slide 5: What exactly is memory?
A memory should have at least three properties.
  1. It should be able to hold a value.
  2. You should be able to read the value that was saved.
  3. You should be able to change the value that’s saved.
We’ll start with the simplest case, a one-bit memory.
  1. It should be able to hold a single bit, 0 or 1.
  2. You should be able to read the bit that was saved.
  3. You should be able to change the value. Since there’s only a single bit, there are only two choices:
    Set the bit to 1
    Reset, or clear, the bit to 0.

## Slide 6: The basic idea of storage
How can a circuit “remember” anything, when it’s just a bunch of gates that produce outputs according to the inputs?
The basic idea is to make a loop, so the circuit outputs are also inputs.
Here is one initial attempt, shown with two equivalent layouts:
Does this satisfy the properties of memory?
  These circuits “remember” Q, because its value never changes.
  (Similarly, Q’ never changes either.)
  We can also “read” Q, by attaching a probe or another circuit.
  But we can’t change Q! There are no external inputs here,
  so we can’t control whether Q=1 or Q=0.

## Slide 7: A really confusing circuit
Let’s use NOR gates instead of inverters. The SR latch below has two inputs S and R, which will let us control the outputs Q and Q’.
Here Q and Q’ feed back into the circuit. They’re not only outputs, but also inputs!
To figure out how Q and Q’ change, we have to look at not only the inputs S and R, but also the current values of Q and Q’:
Qnext = (R + Q’current)’
Q’next = (S + Qcurrent)’
Let’s see how different input values for S and R affect this thing.

## Slide 8: Storing a value: SR = 00
What if S = 0 and R = 0?
The equations on the right reduce to:
Qnext = (0 + Q’current)’ = Qcurrent
Q’next = (0 + Qcurrent)’ = Q’current
So when SR = 00, then Qnext = Qcurrent. Whatever value Q has, it keeps.
This is exactly what we need to store values in the latch.
Qnext = (R + Q’current)’
Q’next = (S + Qcurrent)’

## Slide 9: Setting the latch: SR = 10
What if S = 1 and R = 0?
Since S = 1, Q’next is 0, regardless of Qcurrent:
Q’next = (1 + Qcurrent)’ = 0
Then, this new value of Q’ goes into the top NOR gate, along with R = 0.
Qnext = (0 + 0)’ = 1
So when SR = 10, then Q’next = 0 and Qnext = 1.
This is how you set the latch to 1. The S input stands for “set.”
Notice that it can take up to two steps (two gate delays) from the time S becomes 1 to the time Qnext becomes 1.
But once Qnext becomes 1, the outputs will stop changing. This is a stable state.
Qnext = (R + Q’current)’
Q’next = (S + Qcurrent)’

## Slide 10: Latch delays
Qnext = (R + Q’current)’
Q’next = (S + Qcurrent)’
Timing diagrams are especially useful in understanding how sequential circuits work.
Here is a diagram which shows an example of how our latch outputs change with inputs SR=10.
  0. Suppose that initially, Q = 0 and Q’ = 1.
  1. Since S=1, Q’ will change from 1 to 0 after one NOR-gate delay (marked by vertical lines in the diagram for clarity).
  2. This change in Q’, along with R=0, causes Q to become 1 after another gate delay.
  3. The latch then stabilizes until S or R change again.
S
R
Q
Q’
0 1 2 3 4

## Slide 11: Resetting the latch: SR = 01
What if S = 0 and R = 1?
Since R = 1, Qnext is 0, regardless of Qcurrent:
Qnext = (1 + Q’current)’ = 0
Then, this new value of Q goes into the bottom NOR gate, where S = 0.
Q’next = (0 + 0)’ = 1
So when SR = 01, then Qnext = 0 and Q’next = 1.
This is how you reset, or clear, the latch to 0. The R input stands for “reset.”
Again, it can take two gate delays before a change in R propagates to the output Q’next.
Qnext = (R + Q’current)’
Q’next = (S + Qcurrent)’

## Slide 12: SR latches are memories!
This little table shows that our latch provides everything we need in a memory: we can set it, reset it, and remember the current value.
The output Q represents the data stored in the latch. It is sometimes called the state of the latch.
We can expand the table above into a state table, which explicitly shows that the next values of Q and Q’ depend on their current values, as well as on the inputs S and R.

## Slide 13: SR latches are sequential!
Notice that for inputs SR = 00, the next value of Q could be either 0 or 1, depending on the current value of Q.
So the same inputs can yield different outputs, depending on whether the latch was previously set or reset.
This is very different from the combinational circuits that we’ve seen so far, where the same inputs always yield the same outputs.

## Slide 14: What about SR = 11?
Both Qnext and Q’next will become 0.
This contradicts the assumption that Q and Q’ are always complements.
Another problem is what happens if we then make S = 0 and R = 0 together.
Qnext = (0 + 0)’ = 1
Q’next = (0 + 0)’ = 1
But these new values go back into the NOR gates, and in the next step we get:
Qnext = (0 + 1)’ = 0
Q’next = (0 + 1)’ = 0
The circuit enters an infinite loop, where Q and Q’ cycle between 0 and 1 forever.
This is actually the worst case, but the moral is don’t ever set SR=11!
Qnext = (R + Q’current)’
Q’next = (S + Qcurrent)’
0
0
0
0
0
0
1
1

## Slide 15: S’R’ latch
There are several varieties of latches.
You can use NAND instead of NOR gates to get a S’R’ latch.
This is just like an SR latch, but with inverted inputs, as you can see from the table.
You can derive this table by writing equations for the outputs in terms of the inputs and the current state, just as we did for the SR latch.

## Slide 16: An SR latch with a control input
Here is an SR latch with a control input C.
Notice the hierarchical design!
  The dotted blue box is the S’R’ latch from the previous slide.
  The additional NAND gates are simply used to generate the correct inputs for the S’R’ latch.
The control input acts just like an enable.

## Slide 17: D latch
Finally, a D latch is based on an S’R’ latch. The additional gates generate the S’ and R’ signals, based on inputs D (“data”) and C (“control”).
  When C = 0, S’ and R’ are both 1, so the state Q does not change.
  When C = 1, the latch output Q will equal the input D.
No more messing with one input for set and another input for reset!

## Slide 18: D latch
Finally, a D latch is based on an S’R’ latch. The additional gates generate the S’ and R’ signals, based on inputs D (“data”) and C (“control”).
  When C = 0, S’ and R’ are both 1, so the state Q does not change.
  When C = 1, the latch output Q will equal the input D.
No more messing with one input for set and another input for reset!
Also, this latch has no “bad” input combinations to avoid. Any of the four possible assignments to C and D are valid.

## Slide 19: Sequential circuits and state diagrams
To describe combinational circuits, we used Boolean expressions and truth tables. With sequential circuits, we can still use expression and tables, but we can also use another form called a state diagram.
We draw one node for each state that the circuit can be in. Latches have only two states: Q=0 and Q=1.
Arrows between nodes are labeled with “input/output” and indicate how the circuit changes states and what its outputs are. In this case the state and the output are the same.
This is basically the same as the finite state automata.
Here’s a state diagram for a D latch with inputs D and C.
0x/0
0x/1
Q=0
Q=1
11/1
10/0

## Slide 20: Using latches in real life
We can connect some latches, acting as memory, to an ALU.
Let’s say these latches contain some value that we want to increment.
  The ALU should read the current latch value.
  It applies the “G = X + 1” operation.
  The incremented value is stored back into the latches.
At this point, we have to stop the cycle, so the latch value doesn’t get incremented again by accident.
One convenient way to break the loop is to disable the latches.
+1
ALU
S
X
G
Latches
D
Q
C

## Slide 21: The problem with latches
The problem is exactly when to disable the latches. You have to wait long enough for the ALU to produce its output, but no longer.
  But different ALU operations have different delays. For instance, arithmetic operations might go through an adder, whereas logical operations don’t.
  Changing the ALU implementation, such as using a carry-lookahead adder instead of a ripple-carry adder, also affects the delay.
In general, it’s very difficult to know how long operations take, and how long latches should be enabled for.
+1
ALU
S
X
G
Latches
D
Q
C

## Slide 22: Summary
A sequential circuit has memory. It may respond differently to the same inputs, depending on its current state.
Memories can be created by making circuits with feedback.
  Latches are the simplest memory units, storing individual bits.
  It’s difficult to control the timing of latches in a larger circuit.
Next, we’ll improve upon latches with flip-flops, which change state only at well-defined times. We will then use flip-flops to build all of our sequential circuits.