## Slide 1: Chapter 1 Binary Systems

## Slide 2: Digital Systems
Digital vs. Analog
  Digital: a limited number of discrete values
  Analog: a uncountable number of continuous values
Digits and bits
  Digits: discrete elements
  Bits: binary digits
  Most digital systems use bits to represent information.
   Need to understand the binary system.
Digital computer is a digital system that performs various computational tasks.

## Slide 3: Digital Computers
A computer system is composed of hardware and software.
Hardware
  Consists of electronic components & electromechanical devices.
Software
  Consists of programs composed of a sequential instructions.
  System software
    Collection of programs to make a effective use of computers
    Ex: Operating System, Compilers

## Slide 4: Basic Structure of Digital Computer
Memory
Input Devices
Output Devices
Central Processing Unit (CPU)
Control Unit
(CU)
Arithmetic
Logic Unit
(ALU)

## Slide 5: HW in Digital Systems
Digital/Binary Systems
Computer system, digital TV, digital camera, …
IC (Integrated Circuits)
Combinational
Logic
Sequential Logic
Logic
Gate
Synchronous
Asynchronous
Memory
Memory
Clock
Logic
Gate
Logic
Gate

## Slide 6: Number System
Consists of two things:
  Base or Radix value
  Set of coefficients
Example: the common decimal system
  Base: 10
  Set of coefficients = {0, 1, 2, 3, 4, 5, 6, 7, 8, 9}

## Slide 7: Base-r System
In general, a base-r system
  Base: r
  Set of coefficients = {0, 1, 2, …, r-1}
  Example:
(a5a4a3a2a1a0.a-1a-2a-3)r
= anrn+an-1rn-1+...+a2r2+a1r+a0+a-1r-1+a-2r-2+...+a-mr-m
7392 = 7 × 103 + 3 × 102 + 9 × 101 +2 × 100
(11010.11)2 =1×24+1×23+0×22+1×21+0×20
+1×2-1+1×2-2
= (26.75)10

## Slide 8: Decimal Number System
Consider: 503.21
Arithmetically, shorthand for a radix polynomial:
  5x(102) + 0x(10) + 3x(100) + 2x(10-1) + 1x(10-2)
Other notation: (503.21)10

## Slide 9: Other Number Systems
Binary
  Base: 2
  Set of coefficients = {0, 1}
Octal
  Base: 8
  Set of coefficients = {0, 1, 2, 3, 4, 5, 6, 7}
Hexadecimal
  Base: 16
  Set of coefficients = {0, 1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, F}

## Slide 10: Binary Number
Binary
  Bit: a digit in a binary number
  Byte: 8 bits
  N bits  from 0 to 2N-1
210 = 1Kilo
220 = 1Mega
230 = 1Giga
240 = 1Tera

## Slide 11: Arithmetic Operations in Binary System
The same rules as in decimal
Augend | 101101 | Minuend: | 101101 | Multiplicand: | 1011
Addend | + 100111 | Subtrahend: | - 100111 | Multiplier: | x 101
sum | 1010100 | Difference: | 000110 |  | 1011
 |  |  |  |  | 0000 .
 |  |  |  |  | 1011 .
 |  |  |  | Product: | 110111
0 + 0 = 0 carry=0
0 + 1 = 1 carry=0
1 + 0 = 1 carry=0
1 + 1 = 0 carry=1
0 - 0 = 0 borrow=0
1 - 0 = 1 borrow=0
0 - 1 = 1 borrow=1
1 - 1 = 0 borrow=0
addition
subtraction

## Slide 12: Number Base Conversion
If the number includes a radix point,
Can convert integer part by performing repeated divisions
  Accumulate the remainder digits
Can convert fraction part by performing repeated multiplications
  Accumulate the integer product digits
12043.983
Integer part
Fraction part

## Slide 13: Number Base Conversion
Example: Convert decimal 41 to binary.
 | Integer Quotient |  | Remainder | Coefficient
41/2 = | 20 | + | ½ | a0 = 1
20/2 = | 10 | + | 0 | a1 = 0
10/2 = | 5 | + | 0 | a2 = 0
5/2 = | 2 | + | ½ | a3 = 1
2/2 = | 1 | + | 0 | a4 = 0
1/2 = | 0 | + | ½ | a5 = 1
Integer | Remainder
41 | 
20 | 1
10 | 0
5 | 0
2 | 1
1 | 0
0 | 1
answer : (41)10 = (a5a4a3a2a1a0)2 = (101001)2

## Slide 14: Number Base Conversion
Example1-2: decimal 153 to octal
153 | 
19 | 1
2 | 3
0 | 2 = (231)8

## Slide 15: Number Base Conversion
Example 1-3: (0.6875)10 to binary
Answer:(0.6875)10 = (0.a-1a-2a-3a-4)2 = (0.1011)2
 | Integer |  | Fraction | Coefficient
0.6875 x 2 = | 1 | + | 0.3750 | a-1 = 1
0.3750 x 2 = | 0 | + | 0.7500 | a-2 = 0
0.7500 x 2 = | 1 | + | 0.5000 | a-3 = 1
0.5000 x 2 = | 1 | + | 0.0000 | a-4 = 1

## Slide 16: General Base (Radix) Conversion: Integer Part
Given a value X represented in a source system with radix Bs, represent the same number in a destination system with radix Bd
  Consider the integer part of the number, XI in the Bd system
  R is the Desired digit (LSD)  can repeatedly divide to obtain converted value

## Slide 17: General Base (Radix) Conversion: Fraction Part
  Consider the fraction part of the number, XI in the Bd system
  PI is the desired digit  can multiply by the Bd value

## Slide 18: Octal and Hexadecimal Numbers
Binary-Octal-Hexadecimal

## Slide 19: Octal and Hexadecimal Numbers
Binary to Octal
  Grouping 3 digits in binary and assigning the octal
Binary to Hexadecimal
  Grouping 4 digits in binary and assigning the hexadecimal
( 10 110 001 101 011 . 111 100 000 110 )2 = (26153.7406)8
2 6 1 5 3 7 4 0 6
( 10 1100 0110 1011 . 1111 0010 )2 = (2C6B.F2)16
2 C 6 B F 2

## Slide 20: Complements
Are used in digital computers for simplifying the subtraction and for logical manipulation
Two types of complements for base-r system
  r’s complement
  (r-1)’s complement

## Slide 21: Diminished Radix Complement
Given N in base r having n digits,
  (r-1)’s complement = (rn – 1) – N
  For decimal, 9’s complement
    The 9’s complement of 546700 = 999999-546700=453299
    The 9’s complement of 012398 = 999999- 012398=987601
  For binary, 1’s complement
    Formed by changing 1’s to 0’s and 0s’ to 1’s.
    The 1’s complement of 1011000 = 0100111
    The 1’s complement of 0101101 = 1010010

## Slide 22: Radix Complement
Given N in base r having n digits,
  r’s complement = rn– N
  Adding 1 to (r-1)’s complement
  For decimal, 10’s complement
    The 10’s complement of 012398 = 987602
    The 10’s complement of 246700 = 753300
  For binary, 2’s complement
    The 2’s complement of 1101100 = 0010100
    The 2’s complement of 0110111 = 1001001

## Slide 23: Subtraction Implementation
The direct method of subtraction  borrow concept
  When the minuend digit is smaller than the subtrahend digit, a 1 from a higher significant position is borrowed.
  It works well with paper and pencil.
  How to implement the subtraction with digital hardware ?

## Slide 24: Subtraction with Complements (1)
The subtraction of two n-digit unsigned numbers M - N in base r
  Add the minuend, M, to the r’s complement of the subtrahend.  M + (rn-N) = M – N + rn
  If MN, the sum will produce an end carry, rn, which can be discarded; what is left is the result M – N.
  If M<N, the sum does not produce an end carry and is equal to rn – (N – M ),which is the r’s complement of (N – M); to obtain the answer, take r’s complement of the sum and place a negative sign in front.

## Slide 25: Subtraction with Complements (2)
Using 10’s complement, subtract 72532-3250
Using 10’s complement, subtract 03250-72532
  No end carry: the answer is negative.
   take 10’s complement and place negative sign in front.
  Answer: -69282
M = | 72532
10’s complement of N = | + 96750
Sum = | 169282
Discard end carry 105 = | -100000
Answer = | 69282
In case of MN
M = | 03250
10’s complement of N = | +27468
Sum = | 30718
In case of M<N

## Slide 26: Subtraction with Complements (3)
Subtraction using 2’s complement
  X=1010100 and Y = 1000011
  X-Y
  Y-X
    No end carry
    The answer is Y-X = -(2’s complement of 1101111)=-0010001
X = | 1010100
2’s complement of Y = | +0111101
Sum = | 10010001
Discard end carry 27 = | -10000000
Answer: X-Y = | 0010001
Y = | 1000011
2’s complement of X = | +0101100
Sum = | 1101111

## Slide 27: Subtraction with Complements (4)
Subtraction using 1’s complement
  X=1010100 and Y = 1000011
  X-Y
  Y-X
    No end carry
    The answer is Y-X = -(1’s complement of 1101110)=-0010001
X = | 1010100
1’s complement of Y = | +0111100
Sum = | 10010000
End-around carry = | + 1
Answer: X-Y = | 0010001
Y = | 1000011
1’s complement of X = | +0101011
Sum = | 1101110

## Slide 28: Signed Binary Numbers
How to represent negative numbers?
  In ordinary,
    Positive number: (+) sign
    Negative number: (-) sign
  In computer HW,
    A bit placed in the leftmost position of the number is used for a sign bit.
      Positive: 0
      Negative: 1
  Signed-complement system
    Negative number is indicated by its complement
     2’s complement in the most common
  Three different way to represent -9 with 8bits
    Signed-magnitude: 100010001
    Signed-1’s complement: 11110110
    Signed-2’s complement: 11110111

## Slide 29: Signed Binary Numbers

## Slide 30: Arithmetic Operation of Signed Binary Numbers
Arithmetic addition of two signed binary numbers
  Does not require comparison, only addition.
  A carry out of the sign-bit position is discarded.
Arithmetic subtraction
  (±A)-(+B) = (±A)+(-B)
  (±A)-(-B) = (±A)+(+B)
+6 |  | 00000110 |  | -6 |  | 11111010
+13 |  | 00001101 |  | +13 |  | 00001101
+19 |  | 00010011 |  | +7 |  | 00000111
+6 |  | 00000110 |  | -6 |  | 11111010
-13 |  | 11110011 |  | -13 |  | 11110011
-7 |  | 11111001 |  | -19 |  | 11101101
Carry out is
discarded

## Slide 31: Binary Codes
Digital system manipulates
  not only binary numbers
  but also many other discrete elements of information.
  represented with binary code as symbols.
Code assigning rule
  n-bit binary code  n distinct combinations of 0’s and 1’s
  Each element must be assigned a unique binary bit combination (code): no two elements can have the same value  avoid ambiguity.
  to code 2^n distinct elements
    Minimum number of bits  n bits
    No maximum number of bits

## Slide 32: Binary Coded Decimal (BCD)
Man-Computer Interface
  Man  decimal system
  Computer  binary system
  Needs the conversion of information between them.
  Problem: computer can only accept binary values.
   10 decimal digits are represented with 4-bit binary codes : BCD code
    1010~1111  no use
    (+) input and output data for people
    (-) wasted bits

## Slide 33: BCD Addition/ Decimal Arithmetic
Equal to the binary operation
  Caution: each sum of two digits can not exceed 9
     (1010)2~ (1111)2: no mean in BCD code
  Needs the correction
    The addition of 6 = (0110)2
       Correct the digits and produce carry.
4 |  | 0100 |  | 4 |  | 0100 |  | 8 |  | 1000
+5 |  | +0101 |  | +8 |  | +1000 |  | +9 |  | +1001
9 |  | 1001 |  | 12 |  | 1100 |  | 17 |  | 10001
 |  |  |  |  |  | +0110 |  |  |  | +0110
 |  |  |  |  |  | 10010 |  |  |  | 10111

## Slide 34: Other Decimal Codes
Weighted code
  Each bit position is assigned a weighting factor
  BCD code, 2421 code
Self-complementing code
  9’s complement of a decimal number is obtained directly by switching 1 and 0.
  2421 code, Execess-3 code
BCD code
  Not self-complementing
2421 code
  Some digits can be coded in two possible ways.
Excess-3 code
  Unweighted code  Obtained from the corresponding binary plus 3

## Slide 35: Gray Code
Gray code
  An encoding of numbers so that adjacent numbers have a single digit differing by 1.
  Used for Analog-to-Digital Converter
  Used in application where an error or ambiguity may be produced during the transition.

## Slide 36: ASCII Character Code
  Standard binary code for alphanumeric characters
Notes: 정보교환을 위한 미국 표준 코드이다. 현재 우리가 보는 대부분의 영문과 숫자 코드를 정의함. 7-bit로 충분히 표현이 가능하다. 모든 컴퓨터는 바이트 단위로 처리를 하므로 이 ascii코드도 8bit로 구현이 되면 추가로 얻어지는 코드는 특별한 목적의 응용에 사용이 된다. 즉 그리스 문자나 italic font등에 사용이 된다.

## Slide 37: Error-Detecting Code
To detect errors in data communication or processing
Parity bit: extra bit which makes the total number of 1’s either even or odd.
  Can detect any odd combination errors
  Cannot detect any even combination errors
 | With even parity | With odd parity
ASCII A = 1000001 | 01000001 | 11000001
ASCII T = 1010100 | 11010100 | 01010100

## Slide 38: Binary Storage
Binary cell: a device that possesses two stable states
Cell input: receives data and control signals that set it to one of the states
Cell output: physical quantity indicating which state the cell is in
States are encoded as binary digits {0, 1}

## Slide 39: Registers
Group of n binary cells: an n-bit register
Register has 2n states: all possible n-bit strings
Register state (or content) can be interpreted s value, ASCII, etc
Registers classified as two type of input and output – Serial and/or Parallel
Details on this later in the class

## Slide 40: Register Transfer
Registers are interconnected
  At a given time, content of one register transferred to another
  Content may be transformed/changed during transfer
  Transforming circuit is a data processing or data path element/circuit
Example: Keyboard to register to memory
  Key strike: 8-ASCII to rightmost register
  Key strike: register content shifted left
  4 Key strides: content transferred to memory
Computer must be provided with two devices
  Holding data: register
  Manipulating binary variables: digital logic circuit

## Slide 43: Binary Logic
Deals with variables that have two different values
 typically bits {0, 1}
Logic is based on Boolean Algebra operators
Variables denoted by letters of alphabet
   example: A, B, C, a, b, c, x, y, etc.
Three basic operations considered (for now)
  AND (Boolean algebra multiplication)
  OR (Boolean algebra addition)
  NOT (Boolean algebra inversion)
  More detail in following sections

## Slide 44: Functions
Computers take inputs and produce outputs, just like functions in math!
Mathematical functions can be expressed in two ways:
We can represent logical functions in two analogous ways too:
  A finite, but non-unique Boolean expression.
  A truth table, which will turn out to be unique and finite.
f(x,y) = 2x + y
= x + x + y
= 2(x + y/2)
= ...
An expression is
finite but not unique
A function table is
unique but infinite

## Slide 45: Binary AND Operation
Represented
  by a dot or
  By the absence of operator
  x AND y is equal to z
  z = 1 if and only if x AND y = 1,
  otherwise z = 0

## Slide 46: Binary OR Operation
Represented
  by a plus sign between adjacent variables or constant
  x OR y is equal to z
  z = 1 if x = 1 OR y = 1 OR both x = y = 1,
  otherwise z = 0

## Slide 47: Binary NOT Operation
Represented
  by a prime sign ’ or an overbar
  Unary operator – operates on one variable
  Not x is equal to z
  if x = 1 Then z = 0 Else z = 1,

## Slide 48: Boolean expressions
We can use these basic operations to form more complex expressions:
f(x,y,z) = (x + y’)z + x’
Some terminology and notation:
  f is the name of the function.
  (x,y,z) are the input variables, each representing 1 or 0. Listing the inputs is optional, but sometimes helpful.
  A literal is any occurrence of an input variable or its complement. The function above has four literals: x, y’, z, and x’.
Precedences are important, but not too difficult.
  NOT has the highest precedence, followed by AND, and then OR.
  Fully parenthesized, the function above would be kind of messy:
f(x,y,z) = (((x +(y’))z) + x’)

## Slide 49: Truth tables
A truth table shows all possible inputs and outputs of a function.
Remember that each input variable represents either 1 or 0.
  Because there are only a finite number of values (1 and 0), truth tables themselves are finite.
  A function with n variables has 2n possible combinations of inputs.
Inputs are listed in binary order—in this example, from 000 to 111.
f(0,0,0) = (0 + 1)0 + 1 = 1
f(0,0,1) = (0 + 1)1 + 1 = 1
f(0,1,0) = (0 + 0)0 + 1 = 1
f(0,1,1) = (0 + 0)1 + 1 = 1
f(1,0,0) = (1 + 1)0 + 0 = 0
f(1,0,1) = (1 + 1)1 + 0 = 1
f(1,1,0) = (1 + 0)0 + 0 = 0
f(1,1,1) = (1 + 0)1 + 0 = 1
f(x,y,z) = (x + y’)z + x’

## Slide 50: Truth Tables

## Slide 51: Logic Gates
Electronic circuits operate on 1 or more input signals to produce an output signal.
  Output corresponding to a Boolean operation
Signals: voltages or currents
  Interpreted as a 0 or 1
  Defined by a range of voltage or current values

## Slide 52: Logic Gates
Circuit diagrams use graphical symbols for logic gates
Connections of logic gates between registers can transform data
Logic gates represent interconnections of transistors and other electronic components

## Slide 53: Expressions and circuits
Any Boolean expression can be converted into a circuit by combining basic gates in a relatively straightforward way.
The diagram below shows the inputs and outputs of each gate.
The precedences are explicit in a circuit. Clearly, we have to make sure that the hardware does operations in the right order!
(x + y’)z + x’

## Slide 54: Timing Diagrams
Depict input and output signals as functions of time
Values toggle between two discrete variables

## Slide 55: Multi-input Logic Gates
Can have more than one input
Examples: AND and OR gates